## Slide 1
AIBOTS-2026 HACKATHON | REVIEW 1
Smart Irrigation System Using IoT, Weather API, and Predictive Analytics
An Intelligent Approach to Water-Efficient Agriculture
Team Name: Apex Warrior
Team Members: Manash and Sayak
Institution: KLH University
ESP32 • Soil Moisture Sensing • Weather API • Dashboard
Notes: Good morning judges. We are Team Apex Warrior from KLH University. Our project is an IoT-based irrigation decision-support system: it combines a real soil moisture sensor, air temperature and humidity readings, and weather API data to suggest when irrigation may be needed. It is a monitoring and recommendation system, not a fully automatic controller. Likely question: "Does it water the field automatically?" Answer: Not in this prototype. A pump and relay are future scope.

## Slide 2
Problem Statement
Problem Understanding
AIBOTS-2026 Hackathon | Review 1
“Farmers need an affordable and intelligent irrigation decision-support system that combines soil moisture measurements with weather information to help determine when irrigation may be necessary.”
Irrigating without knowing soil moisture, recent rain or the forecast can lead to:
Unnecessary water use
Water applied when soil is already moist or rain is coming
Higher irrigation cost
More pumping time means more cost
Wasted electricity and resources
Pumps run longer than needed
Hard decisions as weather changes
Rain or heat can quickly change what the crop needs
Relevance: better irrigation decisions support sustainable water management in agriculture.
Notes: Explain that farmers often irrigate by habit or by looking at the field. They may not know the real soil moisture, whether it rained recently, or whether rain is coming. That wastes water, money and electricity. Read the problem statement. We use no statistics here because we do not want unsupported numbers. Criterion: Problem Understanding and Relevance.

## Slide 3
Existing Approaches and Their Limitations
Problem Understanding
AIBOTS-2026 Hackathon | Review 1
Traditional Irrigation
Decisions depend on experience, schedules or visual checks
Soil moisture and weather may not be considered together
Basic Sensor-Based Irrigation
Measures soil moisture
May not account for upcoming rain or wider weather conditions
Proposed Smart Irrigation System
Physical soil moisture sensor
Air temperature and humidity measurement
Weather information through an API
Combines these inputs into recommendations
Our system combines multiple sources of information instead of relying on a fixed schedule or a single sensor reading. Some existing systems may already include weather features.
Notes: Compare the three approaches. Be fair: we do not say all existing systems lack weather integration. Our point is that combining soil sensing, air conditions and forecast in one affordable prototype is useful. Likely question: "Isn't this just a soil sensor?" Answer: A sensor alone cannot know that rain is forecast; we add that context.

## Slide 4
Proposed Solution: End-to-End Workflow
Proposed Solution
AIBOTS-2026 Hackathon | Review 1
1 Soil moisture sensor reads soil values
2 DHT11 reads air temperature and humidity
3 ESP32 reads sensors and connects to Wi-Fi
4 Backend gets current and forecast weather from API
8 LED shows local status using threshold logic
7 Dashboard shows readings, recommendations and alerts
6 Prediction engine estimates irrigation need
5 Software analyzes sensor, rain, temperature, humidity and forecast
Output: monitoring, prediction, alerts and irrigation recommendations. The system does not switch water on or off. The LED is only a status indicator.
Notes: Follow the numbered steps: top row left to right (1 to 4), then the bottom row right to left (5 to 8). Sensors feed the ESP32, the backend adds weather data, the engine produces a recommendation, and the dashboard and LED show the result. Stress that this is recommendation, not automatic control. Criterion: Proposed Solution.

## Slide 5
Hardware Components
Proposed Solution
AIBOTS-2026 Hackathon | Review 1
1
ESP32 Development Board
Main controller; reads sensors; sends readings over Wi-Fi to the backend
2
Soil Moisture Sensor (FC-28 or capacitive)
Gives a moisture-related reading; calibrated to dry / moderate / wet. Capacitive preferred: FC-28 probes can corrode
3
DHT11 Temp & Humidity Sensor
Measures air temperature and relative humidity; helps judge evaporation conditions
4
Breadboard
Easy prototype connections without soldering
5
Male-to-Male Jumper Wires
Connect ESP32, sensors and other components
6
USB Data Cable
Powers the ESP32, uploads code and allows serial debugging
7
LED + 220Ω Resistor
LED shows status (e.g. dry warning); resistor limits LED current
PROPOSED (future)
Water pump and relay module for automatic irrigation. Not part of the current hardware.
Notes: Go through the seven components we have, and what each does. Mention that a capacitive sensor is better long term than the FC-28 because it resists corrosion. The dashed card is a future enhancement, not existing hardware. Likely question: "Why DHT11?" Answer: low cost and enough for a prototype; accuracy is limited, so we treat its readings as approximate.

## Slide 6
Novelty and Innovation
Innovation of the Idea
AIBOTS-2026 Hackathon | Review 1
1 Sensor + weather API integration
Real soil readings with current and forecast weather
2 Weather-aware recommendations
Recent rain and forecast help avoid needless irrigation
3 Real soil moisture monitoring
Physical sensor, not weather-only estimation
4 Environmental analysis
Soil, air temperature and humidity interpreted together
5 Affordable prototype
ESP32 and low-cost components
6 Explainable recommendations
Shows why irrigation is needed or delayed
7 Expandable architecture
Future: crops, history, alerts, pump control
Feature | Basic Sensor System | Proposed System | Status
Soil moisture sensing | Yes | Yes | Hardware available
Air temperature | Depends on components | Yes | Hardware available
Humidity | Depends on components | Yes | Hardware available
Weather API integration | Not always available | Core feature | Planned
Rainfall forecast analysis | Not always available | In proposed workflow | Planned
Dashboard and alerts | Depends on implementation | In proposed workflow | Planned
“Our innovation is the combination of real-time soil moisture sensing, environmental monitoring, and weather forecast analysis in an affordable IoT-based irrigation decision-support system.”
Notes: This slide carries 10 marks for innovation. Our innovation is the combination, not any single part: real soil data plus air data plus forecast, in an affordable, explainable system. The table is honest: green means hardware components we have; orange means software features that are planned, not yet implemented. Likely question: "What is new compared with a basic soil sensor?" Answer: forecast awareness, explanations and an expandable design.

## Slide 7
Hardware and System Architecture
Solution & Architecture
AIBOTS-2026 Hackathon | Review 1
Soil Moisture Sensor
DHT11 Temp & Humidity Sensor
LED + 220Ω Resistor (status only)
ESP32
(GPIO inputs, outputs, Wi-Fi)
ESP32
(GPIO inputs, outputs, Wi-Fi)
Backend / Data Processing (Flask)
Weather API
Wi-Fi / HTTP
Prediction Engine
Web Dashboard & Alerts
Sensor data + weather data are combined in the backend before a recommendation is made
Breadboard + jumper wires
Physical prototype connections between ESP32, sensors and LED.
USB data cable
Powers the ESP32, uploads code and gives serial debugging.
Note
The LED is a status indicator, not a pump. Arrows show data flow.
Diagram shows the proposed design. Backend, API and dashboard are planned components.
Notes: Follow the arrows. The soil sensor and DHT11 send readings to the ESP32. The ESP32 sends data over Wi-Fi to the backend. The backend also pulls weather from the API, and combines both before the prediction engine and dashboard. The LED is driven by an ESP32 output pin as a local status light, not a pump. The breadboard and jumpers form the physical connections; USB provides power and programming. Likely question: "Where is the API key kept?" Answer: in a backend environment variable only.

## Slide 8
Software Architecture and Technology Stack
Solution & Architecture
AIBOTS-2026 Hackathon | Review 1
Frontend
React.js • Tailwind CSS • Chart.js
Backend
Python Flask: sensor-data processing, weather API integration, recommendation logic
Database
SQLite for readings and history, if required
Communication
Wi-Fi • HTTP requests to a backend endpoint
Device Firmware
Arduino IDE or compatible • C/C++ to read sensors and transmit data
Hardware
ESP32 • Soil moisture sensor • DHT11 • LED indicator
All items are proposed technologies; none is claimed as implemented.
The weather API key stays in a backend environment variable, never in frontend code or screenshots.
Notes: Explain the stack from the bottom: hardware, firmware, Wi-Fi/HTTP, Flask backend, optional SQLite, React dashboard. Everything is proposed. Choices are common, free and student-friendly. Security: the API key is stored only on the backend. Likely question: "Why not send data straight to the dashboard?" Answer: the backend combines sensor and weather data and keeps the key private.

## Slide 9
Prediction and Irrigation Decision Logic
Solution & Architecture
AIBOTS-2026 Hackathon | Review 1
Inputs
Soil moisture reading
Air temperature
Relative humidity
Recent rainfall
Weather forecast
Crop type
Soil type
Last irrigation date (if available)
Processing
Calibrate and interpret the soil sensor
Classify soil as dry, moderate or wet
Analyze recent rain and forecast
Consider evaporative demand
Consider crop water needs if known
Combine using transparent rules
Generate recommendation with explanation
Example scenarios
A: Dry soil + no recent rain
Flags a potentially high irrigation need.
B: Moist soil + recent rain
May delay irrigation and keep monitoring.
C: Dry soil + rain forecast
Weighs sensor reading against forecast and suggests a next action.
First prototype: calibrated rule-based logic. Forecasts are uncertain and crop needs vary. Machine learning only if suitable data and evaluation exist. No accuracy is claimed.
Notes: Inputs on the left, processing in the middle, scenarios on the right. Rules are simple and explainable, so a farmer can see why. Scenario C shows why forecast matters: dry soil may still not need water if heavy rain is expected, though forecasts can be wrong. We have not trained any model and quote no accuracy. Likely question: "Why not machine learning?" Answer: we lack labeled training data; rules are transparent and testable now.

## Slide 10
Dashboard and Expected Output
Proposed Design (Mockup)
AIBOTS-2026 Hackathon | Review 1
MOCKUP: illustrative values only, not actual system performance
Soil moisture
-- %
Soil status
Dry / Moderate / Wet
Temperature
-- °C
Humidity
-- %
Recent rainfall
-- mm
Chart: Historical sensor readings (illustrative)
| T-6 | T-5 | T-4 | T-3 | T-2 | T-1 | Now
Soil moisture % (illustrative) | 62 | 58 | 52 | 45 | 38 | 32 | 27
Temperature °C (illustrative) | 28 | 29 | 31 | 32 | 33 | 34 | 34
Soil Status: Dry
Weather: Hot conditions, no significant recent rainfall.
Recommendation: Irrigation may be needed. Check crop requirements and local conditions.
Sensor connection: Connected
LED status: Dry warning
ALERT: Soil moisture has fallen below the dry threshold
Notes: This is a design mockup, not the finished application. It shows the key outputs: current soil reading and status, air temperature, humidity, rainfall, history chart, recommendation, sensor connection status, LED status and a dry-soil alert. All numbers are placeholders. Criterion: Presentation and Clarity, and Proposed Solution.

## Slide 11
Feasibility and Execution Plan
Feasibility & Execution
AIBOTS-2026 Hackathon | Review 1
1
Hardware Setup
Connect sensors to ESP32
Wire LED with 220Ω resistor
Check serial output
2
Sensor Calibration
Collect dry and wet readings
Set thresholds
Verify with chosen soil
3
IoT Communication
Connect ESP32 to Wi-Fi
Send readings to backend
Handle network failures
4
Weather API
Get current and forecast data
Process rain, temp, humidity
5
Recommendation Engine
Combine sensor and weather data
Write transparent rules
6
Dashboard
Show readings and trends
Add warnings and status
7
Testing & Demo
Dry and moist soil tests
Simulate rain and forecasts
Check expected behavior
Phases run in sequence; no completion dates are fixed at Review 1.
Feasible as a student prototype with the listed components and free software tools.
Notes: Seven phases: hardware, calibration, communication, weather API, engine, dashboard, testing. We do not give dates because Review 1 is early. It is feasible because every part uses cheap, common components and free tools. Calibration matters most: we will record dry and wet readings in our own soil. Likely question: "What is the biggest risk?" Answer: sensor accuracy and calibration, so we test with real soil and treat readings as estimates.

## Slide 12
Impact, Future Scope and Conclusion
Impact
AIBOTS-2026 Hackathon | Review 1
Expected benefits
Better-informed irrigation decisions
Potential reduction in unnecessary watering
Real soil readings combined with weather information
Affordable prototyping
Greater awareness of water-efficient practices
Future enhancements (proposed)
Water pump and relay for automatic irrigation
Crop-specific recommendations
Better evapotranspiration estimation
Long-term sensor data analysis
Regional language support
Mobile notifications
Machine learning with labeled data
Additional sensors if required
Automatic pump control is future scope; it needs a pump or valve, relay and safety circuitry.
Smarter Irrigation Starts with Better Information.
Thank You — Questions?
Notes: Summarize benefits: better decisions, less needless watering, real readings plus weather, low cost. Then future scope. Be clear that automatic pumping is not part of the current build. Close with the tagline and invite questions. Likely question: "How much water will it save?" Answer: we do not claim a number yet; we will measure it in testing.